## Slide 1
Program 1
Setting up the Arduino Development Environment.

## Slide 2
Program 2
Setting Up the Arduino Development Environment and Create a Simple Program to Blink an LED.

## Slide 3: Materials Required:
Arduino board (e.g., Arduino Uno)
LED( Built-in LED)
USB cable for connecting the Arduino to the computer
Arduino IDE installed on your computer

## Slide 4: Steps
Connect your Arduino to your computer via USB.
Open the Arduino IDE.
Write the code into the Arduino IDE.
Select the correct board and port from the Tools menu.
Click on the File button, which is present on the menu bar. Click on the Examples. Click on the Basics option and click on the Blink.
Click the Upload button (the right-pointing arrow) to upload the sketch to your Arduino.

## Slide 5
// the setup function runs once when you press reset or power the board
void setup() {
// initialize digital pin LED_BUILTIN as an output.
pinMode(LED_BUILTIN, OUTPUT);
}
// the loop function runs over and over again forever
void loop() {
digitalWrite(LED_BUILTIN, HIGH); // turn the LED on (HIGH is the voltage level)
delay(1000); // wait for a second
digitalWrite(LED_BUILTIN, LOW); // turn the LED off by making the voltage LOW
delay(1000); // wait for a second
}

## Slide 6: Explanation
pinMode(pin, mode): This function configures the specified pin to behave as an input or an output. In this case, the LED is connected to digital pin 13, and it is set as an output.
digitalWrite(pin, value): This function writes a HIGH or LOW value to the specified digital pin. When the pin is set to HIGH, the LED turns on, and when set to LOW, the LED turns off.
delay(milliseconds): This function pauses the program for the specified number of milliseconds. In the code, a delay of 1000 milliseconds (1 second) is used to create the blinking effect.

## Slide 7: Program 3
Setting up the Arduino Development Environment, connecting analog sensors to an Arduino Boarding and reading analog sensor data

## Slide 8: Materials Required:
1 x Arduino board (e.g., Arduino Uno)
1 x Analog sensor (e.g., temperature sensor)
Jumper wires
USB cable for connecting the Arduino to the computer
Arduino IDE installed on your computer

## Slide 9: Steps
Temperature Sensor Connection:
Connect the VCC pin of the sensor to the 5V pin on the Arduino.
Connect the GND pin of the sensor(-) to the ground (GND) on the Arduino.
Connect the output pin of the sensor(S) to the analog pin A0 on the Arduino.

## Slide 10: Continue..
Connect your Arduino to your computer via USB.
Open the Arduino IDE.
Write the code into the Arduino IDE.
Select the correct board and port from the Tools menu.
Click the Upload button (the right-pointing arrow) to upload the sketch to your Arduino.
Open the Serial Monitor (Tools > Serial Monitor) to see the analog readings from the sensor.

## Slide 11
float temp;
int tempPin = 0;
void setup() {
Serial.begin(9600);
}
void loop() {
temp = analogRead(tempPin);
// read analog volt from sensor and save to variable temp
temp = temp * 0.48828125;
// convert the analog volt to its temperature equivalent
Serial.print("TEMPERATURE = ");
Serial.print(temp); // display temperature value
Serial.print("degree C");
Serial.println();
delay(1000); // update sensor reading each one second
}

## Slide 12: Explanation
analogPin: The pin where the sensor is connected. In this example, it's connected to pin A0, but you can change it to any other analog pin (A0 to A5 on most Arduinos).
Serial.begin(9600): Initializes serial communication at a data rate of 9600 bps. This is necessary to print the values to the Serial Monitor.
analogRead(analogPin): Reads the analog value from the specified pin. The value ranges from 0 to 1023, corresponding to 0V to 5V.
Serial.println(sensor Value): Prints the sensor value to the Serial Monitor.
delay(100): Adds a delay of 100 milliseconds between readings. This is optional and can be adjusted or removed.